# SET UP LEADER

Positioned Assigned To: You Report To: (Decon Group Director)

Mission:	Effectively and efficiently provide for decontamination of patients by establishing decontamination perimeter and activating or deploying Decon showers

____ Report to HazMat Decon Room

- Request and receive incident briefing from Decon Group Director.

- Receive Set Up Leader Checklist.

____ Assign Team members as needed for completion of tasks.  Need at a minimum 4 people for setup

____ Request Security to lock the POB North entrance

____ Select location for Decon shower set-up (See Attachment I)

____ Supervise the set up of Decon showers, connect water supply and route hoses

____ Set-up supplies for the following:

- ____ Drums (x2) for contaminated clothing and personal items

- ____ Drums (x2) for used PPE

- ____ Table at entrances to Decon area

- ____ Collapsible roller system for non-ambulatory

- ____ Transfer (x2) Boards

____ Set-up barricades and poles with tape to direct foot traffic.  Barricades located in tractor barn. Poles and tape in Hazmat Room

____ Set-up signs delineating corridor (outline path from cold zone to Emergency Department)

- Use colored tape and poles (located in storage room), if able

____ Put up signs directing victims to Decon area

____ Retrieve ID supplies / materials for ID of victims:

- Markers

- Triage Tags for patient identification

- Plastic Bags (small personal items and large clothing)

- Patient Information cards (English & Spanish)

____ Establish Rest area for members of HazMat team

- Request chairs if needing more

___ 	Mix water and soap (Dawn for drills, MDP for real) in sprayers for cleaning the patients and Decon members. Another sprayer could be used for MDP for cleaning equipment etc. DIRECTIONS: Combine Parts A and B equally on MDP.

____ Reassign Team members to Decon or Support Teams as needed

____ Brief team members on duties/responsibilities