POLICY

It is the policy of <<Facility Name>> to provide and maintain systems for extinguishing fires.

## PURPOSE

The purpose of this policy is to require that any Fire Protection System is designed, installed, maintained, and tested in accordance with all applicable standards. Fire Protection Systems equipment maintenance and testing will be by established schedule in the appropriate Chapter of the NFPA® standard for the system type specified.

RESPONSIBILITY

The <<Facilities Department>> is responsible for providing and maintaining systems for extinguishing fires.

PROCEDURE

The organization ensures the proper design, installation, maintenance, and testing of its’ fire protection systems through a variety of processes including but not limited to pre-design meetings, design review, acceptance testing, and routine maintenance in accordance with NFPA standards.  This applies to all types of suppression/protection systems used including wet pipe, dry pipe, chemical, and other gaseous systems.

- For new construction, the fire alarm system monitors the components of any required approved automatic sprinkler system. (For full text, refer to NFPA 101-2012: 20/21.3.5.2; 9.7.1.1)

- The fire alarm system is connected to water flow alarms of any required automatic sprinkler system. (For full text, refer to NFPA 101-2012: 20/21.3.4.4; 20/21.3.5; 9.7.1.1)

- Piping supports for approved automatic sprinkler systems are not damaged or loose. (For full text, refer to NFPA 101-2012:20/21.3.4.4; NFPA 25-2011: 5.2.1; 5.2.2; 5.2.3)

- Approved automatic sprinkler systems piping is not used to support any other item. (For full text, refer to NFPA 101-2012: 20/21.3.4.4; NFPA 25-2011: 5.2.2; NFPA 13-2010: 8.5.5.2; 8.5.5.3)

- Sprinkler heads are not damaged and are free from corrosion, foreign materials, and paint. (For full text, refer to NFPA 101-2012: 20/21.3.4.4; NFPA 25-2011: 5.2.1; 5.2.2; NFPA 13-2010: 6.2.6.2; 6.2.7.1)

- There is 18 inches or more of open space maintained below a sprinkler deflector to the top of storage. Note: Perimeter wall shelving may extend up to the ceiling when not located directly below a sprinkler head. (For full text, refer to NFPA 101-2012: 20/21.3.4.4; NFPA 25-2011: 5.2.1; 5.2.2; NFPA 13-2010: 8.5.5; 8.5.6)

- The travel distance from any point to the nearest portable fire extinguisher is 75 feet or less. Portable fire extinguishers have appropriate signage, are installed in a cabinet or secured on a hanger made for the extinguisher and are at least four inches off the floor. Those fire extinguishers that are 40 pounds or less are installed so the top is not more than 5 feet above the floor.

(For full text, refer to NFPA 101-2012: 20/21.3.5.3; 9.7.4.1; NFPA 10-2010: 6.1.3; 6.2.1)

- The hospital meets all other Life Safety Code extinguishing requirements related to NFPA 101-2012: 20/21.3.5.