POLICY

It is the policy of <<Facility Name>> to maintain and operate all equipment in accordance with the manufacturer’s recommendations and safe manner.

PURPOSE

Equipment that operates with water that can be aerosolized (e. g., cooling towers, faucets, showers, fountains, pools, spas) may become contaminated with potentially infectious biological agents even though the equipment is operated within the manufacturer’s guidelines.  Regular maintenance and cleaning of the equipment and proper treatment of the water will be performed to ensure that the risks of hazards are minimized to the staff, patients and visitors of <<Facility Name>>.

PROCEDURE

## Treatment & General Cleaning

Cooling towers, water display fountains, spas, pools, and other open water systems that can generate aerosols shall have a maintenance program that includes routine cleaning of the water reservoir and piping systems.  The maintenance shall be conducted in accordance with the manufacturer’s recommendations and appropriate cleaning instructions.  When necessary, make up water should be provided from the normal water service system.  Open-water systems that have been out of service for an extended period of time shall be thoroughly cleaned before being returned to service.

Systems that generate or utilize aerosolized potable tap water (showers, drinking fountains, ice machines, tap water faucets) shall be properly cleaned and maintained to control the contamination from potentially infectious biological agents if out of service for a period of time.  Water storage tanks (hot water systems, reserve storage tanks) that are not continually utilized should be routinely cleaned and decontamination.

During maintenance and cleaning procedures, the appropriate personnel protection equipment (PPE) shall be worn to prevent exposure to potentially infectious biological agents, such as Legionella, Mycobacterium, and Pseudomonas.

- Treatment

The water treatment program should include the routine application of the appropriate biocide treatment agents designed to eliminate and control biological agents and other contaminates that can accumulate from exposure to the open atmosphere.  During the application of treatment and cleaning agents, the appropriate PPE shall be worn.

- Documentation

Routine maintenance and treatment procedures of cooling towers and other open water systems shall be recorded.  Date of service, service and treatment activity, and personnel conducting the service shall be recorded.  Maintenance and cleaning of open water or potable water systems that have been out of service for an extended period to time shall also be documented.

- Staff Training

Staff members responsible for the water treatment program will be trained during orientation and receive appropriate training thereafter regarding proper cleaning and maintenance procedures, and the safe handling and proper application of water treatment and cleaning chemicals.  All guidelines for handling hazardous materials and the recommendations for proper use of PPE will be presented.

ATTACHMENT:

Attachment I- Risk Assessment for Waterborne Organisms in a Domestic Water System

(UT-EC.02.05.01EP14 b)