# POLICY

# It is the policy of <<Facility Name>> that extension cords are not used as a substitute for fixed wiring in a building. Extension cords which have been approved for temporary use are removed immediately upon completion of the intended purpose.

# PROCEDURE

- Suitable extension cords for temporary use are available in the <<Name Department>>. These cords are grounded three-wire, UL Listed (or equivalent), and may not be modified from their original intended use, size, etc.

- Extension cords will be visually inspected for frayed wires, exposed parts, pinching, etc. prior to each use. Damaged cords will be cut (to avoid future use) and disposed.

- Extension cords will not be used in conjunction with Relocatable Power Taps (RPTs) or daisy-chained into one another.

- Extension cords will not be used with heat-producing devices such as, but not limited to toasters, microwave ovens, coffee pots, and portable space heaters (where allowed).

- Diligent care must be utilized when extension cords are in use including avoidance of trip hazards, which may require the use of an appropriate tape to secure the temporary cord.

- Extension cords should not be run through doorways, ceilings, walls, etc. (without permission from <<Name Department>>.

- Considerations for use of extension cords during construction or renovation projects is conducted during project assessment.