POLICY

<<Facility Name>> provides and maintains building features to protect individuals from the hazards of fire and smoke in Business Occupancies particularly as it relates to hazardous areas.

PURPOSE

All hazardous areas shall be protected in accordance with NFPA 101 2012 edition, 38.3.2 and 39.3.2.   In addition, interior finishes need to be controlled to minimize smoke and toxic gases. Openings are necessary and include such features as heating, ventilating, and air conditioning (HVAC) systems, elevator shafts, and trash and laundry chutes.

PROCEDURE

The organization ensures the maintenance of building features for the protection of individuals from the

hazards of fire and smoke through numerous processes related to the design, maintenance, surveillance, and management of Life Safety Code issues, including but not limited to vertical openings, hazardous areas, interior finish, walls and partitions, smoke compartmentation, fire and smoke dampers, fire walls, floor/ceiling assemblies, etc.

- All hazardous areas are enclosed with one-hour fire-rated walls with ¾-hour fire-rated doors; or hazardous areas have sprinkler systems and are constructed to resist the passage of smoke with doors equipped with self-closing or automatic-closing devices. (For full text, refer to NFPA 101-2012:  38/39)

- Interior wall and ceiling finishes must be Class A or B for exit and exit access corridors. All other areas should be class A, B, or C.

- Alcohol-based hand rubs (ABHR) are stored and handled in accordance with NFPA 101-2012: 8.7.3.1, and as follows:

- Corridor clear width of at least 44 inches is not compromised by dispenser.

- ABHR does not exceed 95% alcohol.

- Maximum individual dispenser capacity is 0.32 gallon of fluid (0.53 gallon in suites or rooms separated from corridors) or 18 ounces of NFPA Level 1–classified aerosols.

- Dispensers have a minimum of four feet of horizontal spacing between them.

- Dispensers are not installed within one inch of an ignition source.

- Operation of the dispenser must comply with the manufacturers’ instructions for use.

- ABHR is protected against inappropriate access.

- Not more than an aggregate of 10 gallons of fluid or 135 ounces of aerosol are used on a single story or in a single smoke compartment outside a storage cabinet, excluding one individual dispenser per room.

- Storing more than five gallons of fluid in a single story or a single fire compartment complies with NFPA 30.

- The hospital meets all other Life Safety Code fire and smoke protection requirements related to NFPA 101-2012: