DECON Reeves Tent Setup

- Lay out a tarp to protect the tent.

- Lay out the berm (black tarp-looking)

  - Sides – Collapsed and flipped under

  - Entrance/Exit – Collapsed and flipped forward

  - Yellow safety markings facing upward

- Put the tent in the middle of the berm

- Remove 4 white tent poles

- Wire loops in a row indicate side walls

- Loosen straps

- Have one person at each corner

- Lift and expand shelter by walking backward

- Flip doors and side fabric over so they are hanging down

- 2 red tab lifting points are located on each end

- Lifting together, place white poles under red tabs for support (they do not insert into holes)

- Center shower wands, shower heads, and lights can be installed:

  - The 2 red ones are injected solution lines

  - The 2 black ones are rinsed lines

  - These are installed for non-ambulatory patients.  Red is the entrance, black is the exit.

- Now lift the shelter with poles until the side walls are level on the ground.  There is no click when extended up.

- Berm walls can now be set up around side walls up around.  Side walls up first, one entrance left down for setup.

Grids:

- Place down grids on both sides of rollers and all flooring all around.

- Put up entrance berm

- Place submersible pump inside at lowest corner and attach discharge hose

- Install lane curtains and anchor cords to the grid

DECON Tent Teardown

Let the tent dry out before storing it:

- Remove Curtains

- Remove wands and showerheads and replace them with caps

- Remove the discharge hose from the pump and remove the pump from the berm

- Remove grids and rollers

- Collapse side walls under

- Collapse entrance/exit wall forward

- Lift corners of the shelter and flap over the berm so it can be collapsed

- Lift side walls over the berm

- Locate striking positions (2 on each side).  Place a hand under the flap

- SAFETY: No one inside can be inside and ensure before the collapse

- Lift and step back to strike out for collapse

- Lift shelter and walk inward

- Place straps (2) around and cinch up

- Place on the side and re-cinch

- Put a bag over the shelter after standing shelter up

- Lay down the shelter and put poles in the bag

- Cinch tie on top of the box

- Tighten outside straps

- Fold the berm lengthwise in quarters.

Collapsible Rollers:

- Expand and center

- Adjust height, locate second locking, slide up the ring, and turn the knob inside to tighten.

- Turn wheels inside.