~Building Services

Standard LS.03.01.50

The hospital provides and maintains building services to protect individuals from the hazards of fire and smoke.

Note 1: This standard applies to sites of care where four or more [patient]s at the same time are provided either anesthesia or outpatient services that render [patient]s incapable of saving themselves in an emergency in the organization.

Note 2: This standard applies to all hospitals seeking accreditation for Medicare certification purposes, regardless of the number of [patients]s rendered incapable.

Note 3: In leased facilities, the elements of performance of this standard apply only to the space in which the accredited organization is located; all exits from the space to the outside at grade level; and any Life Safety Code building systems that support the space (for example, fire alarm system, automatic sprinkler system).

LS.03.01.50EP1-Equipment using gas or related gas piping complies with NFPA 54-2012, National Fuel Gas Code; electrical wiring and equipment complies with NFPA 70-2012, National Electric Code. Existing installations can continue in service provided there are no life-threatening hazards. (For full text refer to NFPA 101-2012: 20/21.5.1; 9.1.1)

LS.03.01.50EP2-Heating, ventilation and air conditioning (HVAC) comply with NFPA 101-2012: 9.2 and are installed in accordance with manufacturers’ specifications. (For full text refer to NFPA 101-2012: 20/21.5.2.1; 9.2)

LS.03.01.50EP3-Any heating device (other than a central heating plant) is designed and installed so combustible materials cannot be ignited by the device, and safety features stop fuel and shut down equipment if it experiences excessive temperature or ignition failure.

Note: If fuel-fired, the heating device is designed as follows:

- Chimney or vent connected

- Takes air for combustion from outside

- Combustion system that is separate from occupied area atmosphere

(Please note: for full text refer to NFPA 101-2012: 20/21.5.2.2)

LS.03.01.50EP4-A suspended unit heater(s) is permitted provided the following conditions are met:

- Not located in means of egress or patient rooms

- Located high enough to be out of reach of people in the area

- Has a safety feature to stop fuel and shut down equipment if it experiences excessive temperature or ignition failure

(Please note: for full text refer to NFPA 101-2012: 20/21.5.2.2)

LS.03.01.50EP5-New elevators are equipped with all of the following:

- Firefighters service key recall and smoke detector automatic recalls

- Firefighters service emergency in-car key operation

- Machine room smoke detectors

- Elevator lobby smoke detectors

Existing elevators meet these requirements when they have a travel distance of 25 feet or more above or below the level that best serves the needs of the firefighters. (For full text refer to NFPA 101-2012L 20/21.5.3; 9.4.2)

LS.03.01.50EP6-Escalators, dumbwaiters, and moving walks comply with the provisions of 9.4. All existing escalators, dumbwaiters, and moving walks (including escalator emergency stop buttons and automatic skirt obstruction stop) conform to the requirements of ASME/ANSI A17.3, Safety Code for Existing Elevators and Escalators. (For full text, refer to NFPA 101-2012: 20/21.5.3; 9.4.2)

LS.03.01.50EP7-The hospital does not allow unvented fuel-fired heaters. (For full text refer to NFPA 101-2012: 20/21.5.2.2)

LS.03.01.50EP8-All heating appliances are provided with safety features to stop the flow of fuel and turn off the appliance during times of excessive temperatures or ignition failure. (For full text refer to NFPA 101-2012: 20/21.5.2.2)

LS.03.01.50EP9-Waste chutes are installed per NFPA 101-2012: 9.5 and meet the following requirements:

- Walls, partitions, and inlet openings meet the requirements of NFPA 101-2012: 8.3

- Doors of chutes open to a room designated exclusively for accessing the chute opening

- Rooms used for accessing the chute opening(s) are separated from other spaces per NFPA 101-2012: 8.7

- Chutes are permitted to open in rooms not exceeding 400 cubic feet in size if the room is sprinkler protected and not used for storage.

For full text refer to NFPA 101-2012l 20/21.55.4; 9.5; NFPA 82-2009)

Note: Existing installations having properly enclosed and maintained chute openings are permitted to have inlets open to a corridor or normally occupied space.

LS.03.01.50EP10-The hospital meets all other Life Safety Code building service requirements related to NFPA 101-2012:  20/21.5.

### Recommended Documents:

Policy for determining compliance

Examples:

BS-LS.03.01.50 EP1-10 a Building Services