POLICY

Each operational component of a utility system on the inventory will be tested to assure all performance and safety specifications are met before initial use.

# TESTING ON DELIVERY

Each operational component of utility systems will be tested by <<Engineering Department>> before initial use and after major repairs or upgrades.

- All operational components will be inspected upon delivery for damage.  Damaged goods will be returned to the supplier.

- The <<Engineering Department>> and the vendor will unpack and inspect the equipment for hidden damages.  In addition, the <<Engineering Department>> will determine if all required operating and service information were supplied with the equipment.  If any damage is observed, or documentation is missing, the <<Engineering Department>> will notify <<purchasing group, e.g. Purchasing Department>>.  The <<Purchasing Department>> will notify the supplier to take necessary action.

- The <<Engineering Department>> will conduct appropriate performance and safety inspections, and calibration checks.  When it is determined that the equipment meets all requirements for performance and safety, the <<Engineering Department>> will release the equipment for use.

- The completion date and results of the test will be documented and maintained by the <<Engineering Department>>.

# TESTING OF INSTALLED SYSTEMS

- All fixed and mounted equipment will be installed as specified in the purchasing agreement.

- The manufacturer, supplier, or the <<Engineering Department>> will install or mount the equipment as required.

- All required power and signal lines will be installed and certified as specified in the purchasing agreement.

- All fixed and mounted equipment will be tested for performance and safety as specified in the purchasing agreement. The <<Engineering Department>> and appropriate engineering staff will witness all certification testing and calibration not performed by hospital staff.

- The completion date and results of the test will be documented and maintained by the <<Engineering Department>>.