# POLICY

It is the policy of <<Facility Name>> that all piped medical gas systems shall be tested when installed, modified, or repaired before being placed into service.

PURPOSE

All piped medical gas systems shall be tested when installed, modified, or repaired before being placed into service to protect patients, staff, and visitors.  The data will be documented.  The following will be checked at a minimum:

- Purity

- Correct gas

- Proper pressures

All medical gas systems, which have been installed, repaired, or modified, shall be tested per NFPA 99-2012, Chapter 5 before being placed into service.

PROCEDURE

- No scheduled repair, modification, or installation work shall be allowed to begin on any piped medical gas system without the permission of the <<Engineering Director>> or designee.

- No medical gas system shall be placed into service without the permission of the <<Engineering Director>>.  This permission shall not be granted until all testing documentation, indicating that the system(s) are compliant, has been delivered to the <<Engineering Director>>.

- The following activities will be followed:

  - All piped medical gas systems shall be installed, modified, or repaired by qualified personnel as defined by NFPA 99-2012, Chapter 5.

  - All piped medical gas systems shall be tested, per NFPA 99-2012, Chapter 5, before being placed into service.  These tests shall include cross-connection testing, piping purity testing, and pressure testing.

  - All medical gas systems shall be labeled per NFPA 99-2012, Chapter 5.  Zone valve labeling shall include the exact rooms or areas which are served by the load side of the zone valve(s).

  - The testing and results documentation will be maintained in the <<Engineering>> department.  Documentation may also be kept in the construction file for the project.